## Slide 1: Long-wave infrared nonlinear optics program at Stony Brook University
Ilan Ben-Zvi
ONR MURI Kick-off meeting
UCLA

## Slide 2: Proposed projects in long-wave IR nonlinear optics at Stony Brook University
Self-guiding of 1-10 TW, picosecond CO2 laser pulses over 100 m in air at the BNL ATF II in collaboration with the UCLA group and other MURI collaborators
Development of a 100 MW, high-repetition rate (5 Hz), 200 ps, 9 – 10 µm and 4 – 5 µm CO2 laser system at the UCLA Neptune Laboratory (while ATF II is coming on line)
Apply 100 MW source for measurements of the of the nonlinear refractive index of atomic and molecular gases from 4 – 5 µm and 9 – 10 µm at UCLA

## Slide 3: Self-guiding of 1-10 TW CO2 laser pulses over 100 m in the air at BNL ATF II
Goals
Demonstrate guiding over 100 m in the air using 1-10 TW pulses
  - Pcrit ~0.5 TW
Diagnose LWIR radiation after nonlinear propagation
  Spatial
  Spectral
  Temporal

## Slide 4: 10 TW CO2 laser system at the BNL ATF II
30 – 50 J, 3 – 5 ps
10 TW
(Pcrit ~ 0.5 TW in air)

## Slide 5: Self-guiding of 1-10 TW CO2 laser pulses over 100 m in the air at BNL ATF II
Timeline for experiments
ATF II will be available for experiments in 2019 or even later
Research effort prior to this date will be dedicated to nonlinear refractive index measurements at UCLA
What is Pcrit in the IR?

## Slide 6: Development of a high-repetition rate (5 Hz), high-power, tunable IR source at UCLA Neptune Laboratory
Goals
Design a high-repetition rate (5 Hz), tunable CO2 laser MOPA using existing hardware at UCLA, independent from UCLA’s current picosecond CO2 laser system.
  Source will be designed for nonlinear refractive index measurements in gases over a range of IR wavelengths (4 – 5 µm and 9 – 10 µm)
Produce 100 MW, 200 ps CO2 laser pulses from 9 – 10 µm
Apply high-power 9 – 10 µm pulses to produce ~ 20 MW, 200 ps 4 – 5 µm radiation by efficient second harmonic generation

## Slide 7: Development of a high-repetition rate (5 Hz), high-power, tunable IR source at UCLA Neptune Laboratory
1 µm Nd:YAG
CO2 master oscillator
Semiconductor slicing
Optical parametric amplifier
500 ns
9-10 µm pulse
TEA CO2 laser final amplifier
Field broadened
Second harmonic crystal
200 ps
9-10 µm pulse
100 MW, 200 ps
9-10 µm pulse
~20 MW, 200 ps
4-5 µm pulse

## Slide 8: Measurements of the of the nonlinear refractive index of atomic and molecular gases in the infrared (at UCLA)
Goals
Nonlinear refractive index measurements of atomic and molecular gases using third-harmonic generation at 1 µm, 4 – 5 µm, and 9 – 10 µm
  - What is the dispersion of n2 in the infrared?
  IR resonances of minor air constituents such as CO2, H2O, and NH3 may affect the nonlinearity of air
Pump-probe experiments to measure the time dependence of the nonlinear response of molecular gases pumped by IR radiation in 9 – 10 µm and 4 – 5 µm range
  Probed using 1 µm, picosecond interferometry
    Probe sampled from laser system front end, deterministically synchronized with IR pump

## Slide 9: Conclusions
Stony Brook University will lead effort on self-guiding at BNL ATF II
To demonstrate self-guiding of 1 – 10 TW CO2 laser pulses over 100 m in the air and to diagnose spatial, spectral, and temporal properties of guided radiation.
  ATF II will become available in 2019
Prior to ATF II experiments Stony Brook University will perform nonlinear refractive index measurements at UCLA
Develop an independent, high-repetition rate, tunable source of high-power IR radiation from 9 – 10 µm and 4 – 5 µm at UCLA.
Measure n2 of atomic and molecular gases in the IR spectral range.