## Slide 1: LWIR Nonlinear Optics in gases: Theory and Simulations
Jerome V Moloney
College of Optical Sciences
Arizona Center for Mathematical Sciences
Funding: MURI Award N00014-17-1-2705; AFOSR Support FA9550-16-1-0088
UCLA Lead: “Fundamental Studies of Nonlinear Optics and Laser-plasma Phenomena in Gases and Solids Using High-Power LWIR Lasers”
Research Team: M. Kolesik co-PI (OSC), S.W. Koch (Marburg), E.M Wright (OSC)
Senior Researcher/Postdocs: C. Dineen, K. Schuh, P. Rosenow, P. Panagiotopolous
Grad Students: A. Hofstrand (Appl. Math), J. Nehls (OSC)
UCLA MURI Kickoff 2017

## Slide 2: Talk Overview
Introduction
Background Theory
Developing light-matter coupling models [Task T2.2/T4.2]
Simulating 10µm Ultrashort Pulse Atmospheric Propagation [Task T3.4]
Conclusion

## Slide 3: Research Overview
Our team has identified significant paradigm shifts modifying the physics of long range multi-TW pulse propagation at longer MWIR and LWIR wavelengths:
The new physics that emerges includes:
Optical carrier wave shocks – emitted dispersive waves facilitate low loss propagation
- P. Panagiotopoulos, P. Whalen, M. Kolesik, and J. V. Moloney, Nat Photon 9, 543-548 (2015).
Many-body Coulomb mediated dephasing of freed electrons significantly suppresses the nonlinear
induced Kerr self-focusing lens that confines the beam. – multi-km whole beam self-trapping.
- K. Schuh, M. Kolesik, E.M. Wright, S.W. Koch and J.V. Moloney, Phys. Rev. Lett., 118, 063901 (2017).
Important consequence: Higher power/energy low-loss transport over longer propagation paths within key atmospheric transmission windows.
Current LWIR USP sources power/energy limited:
10 µm CO2 45J 3 ps source at UCLA – launch beam issues, Brookhaven National Lab
10 µm CO2 multi-Joule few ps source being developed jointly by NRL/AFRL – Victor Hasson consultant
Expected delivery to Dr. Andreas Schmitt-Sody AFRL

## Slide 4
Atmospheric Transmission Windows (HITRAN)
CO2 Asymmetric stretch
8 – 12 µm Transmission
MWIR LWIR

## Slide 5: IR vs Mid-IR Atmospheric Filament Scaling
Ionization loss limits path length
Low loss propagation

## Slide 6: Chaotic Filamentation in 800nm TW Pulses
Veins are elevated ridges of
intensity on which modulational
instabilities grow
Intense self-focused
filaments
NRL Laser Parameters
Pulse energy = 1.425 J
Pulse length = 400 fsec
Peak power = 3.56 TW
Propagation distance = 10 m
Relative disposition of filaments dictated by initial aberrations
across the beam
D.E. Roskey, M. Kolesik, J.V Moloney and E.M Wright
Appl. Phys. B 86 249 (2007)
Broad background acts as an energy reservoir (photon bath) to sustain recurring filaments
M. Mlejnek, M. Kolesik, J.V. Moloney, E.M. Wright, PRL, 83(15) pp. 2938-2941 (1999).
Individual filaments last for less than 1 m!
Whole beam diffraction limits range.

## Slide 7: Extended 3D NLSE Model - IR Filaments
Diffraction
GVD
Kerr Nonlinearity
Plasma Absorption/
refraction
Multi-photon absorption
Delayed Raman Response
- Plasma Drude Model
Avalanche generation
Multi-photon generation
Plasma recombination
M. Mlejnek, M. Kolesik, J.V. Moloney, and E.M. Wright, PRL,83(15) pp. 2938-2941 (1999).

## Slide 8: Adaptive Mesh GNLSE Parallel Solver
Dynamic regriding in space and time – Multiple light strings
M. Mlejnek, M. Kolesik, J.V. Moloney, E.M. Wright, PRL, 83(15) pp. 2938-2941 (1999).

## Slide 9: Talk Overview
Introduction
Background Theory
Developing light-matter coupling models [Task T2.2/T4.2]
Simulating 10µm Ultrashort Pulse Atmospheric Propagation [Task T3.4]
Conclusion

## Slide 10: Filament Modeling Hierarchy
Nonlinear Envelope Equation – Generalization of Nonlinear Schrödinger Equation
- Computational workhorse for near-IR filament propagation
J.V. Moloney and A.C. Newell, “Nonlinear Optics”, Perseus (2004)
Dispersion operator (normal or anomalous GVD)
Diffraction
Nonlinearity

## Slide 11
Unidirectional Pulse Propagating Equation (z-UPPE)
Plasma-related current
Nonlinear polarization evaluated from real field
Accurate chromatic dispersion
Second Harmonic component = source of TH
Carrier based approach, no envelope approximations used
Scalar UPPE Model (Unidirectional)

## Slide 12
UPPE Carrier Shock Regularization – No HOKE or Ionization Regularization Necessary
Weak dispersion of
ionized electrons
works in conjunction
Intrinsic GVD
Long wavelength limit of NLSE supports Luther et al. analysis (1994)

## Slide 13: Beyond UPPE – Bidirectional Pulse Propagation
Modeling the scattering of nonlinear ultra-short laser pulses from remote targets Andrew Hofstrand, UA
M. Kolesik, J.V. Moloney, “Nonlinear optical pulse propagation: From Maxwell's to unidirectional equations”, Phys. Rev E., 70, 036604 (2004).

## Slide 14: Modulational Instability – Filament waist scaling
Gain of perturbed transverse wavenumbers
Most unstable wavenumber growth rate
Linearize NLSE around an infinite planewave:
Observation:
Unstable transverse wavenumber domain shrinks with increasing wavelength.
Transverse size of perturbation grows with

## Slide 15: Shock Singularity: infinite slope
Burger’s Equation:
Shock regularization:
Korteweg – deVries (KdV):
Shallow water waves - Dispersive regularization
Optical carrier

## Slide 16: Modified Kadomtsev-Petviashvili (MKP1)
Canonical Full Field Propagator for long wavelength USPs
Asymptotic limit of UPPE for strongly nonlinear weakly dispersive waves
- K. Glasner et al, Int. J. Optics. http://dx.doi.org/10.1155/2012/868274 (2011)
Exhibits carrier shock + blowup - Originally derived for ion-acoustic waves
P. Whalen et al., Phys.Rev.A, 89, 023850 (2014); P. Panagiotopoulos et al. JOSAB, 32, 1718 (2015)
Balakin, A.A., A.G. Litvak, V.A. Mironov, S.A. Skobelev. JETP, 2007, 104 363-378
Carrier shock in Diamond at 8µm

## Slide 17
Shock region
+ Collapse
Collapse
region
Shock Regularization is Universal for Long Wavelengths
NLSE, NEE etc
MKP
UPPE
LNL > LDisp
LNL < LDisp

## Slide 18: Talk Overview
Introduction
Background Theory
Developing light-matter coupling models [Task T2.2/T4.2]
Simulating 10µm Ultrashort Pulse Atmospheric Propagation [Task T3.4]
Conclusion

## Slide 19
QM-models:
atoms and molecules
2S
2P
Non-Hermitian Quantum Mechanics
One-time system characterization
Metastable Electronic State Approach
F
Metastable State:
Response to optical field
Experimental verification,
Time-space resolved comparison
Application: Large-scale simulations,
MESA=Module for gUPPE simulator
Guided by exact results
Kolesik Group:

## Slide 20
Experiment vs MESA comparison, high-intensity example
Transverse profiles at different times
Temporal profile
Plasma
Kerr vs Plasma
Kerr
This case tests:
Nonlinear index
Ionization rate
Competition between
Exp.
Sim.
Kolesik Group:
Expt:Milchberg

## Slide 21
Experiment vs MESA comparison, “global picture”
Ar
Kr
Xe
Plasma
Kerr
Measured and simulated transient phase shifts versus pump intensity

## Slide 22
Atomic gases and Single-Active Electron:
Potentials available for inert gases
Relatively easy one-time characterization for MESA
Comparison with experiments justifies SAE
No real need to go beyond SAE
Molecules in MESA:
Only parameterized SAE potentials available
Results qualitatively OK
Quantitatively, N2 nonlinear index systematically too high
Ab initio can provide necessary data
Q: SAE versus ab initio

## Slide 23
MESA model for molecular nitrogen
Inputs:
haCC method (A. Scrinzi group)
Multi-electron
Captures ionizing states
Ab inito, no adjustable parameters
Outputs:
Linear polarizability (vs angle)
Nonlinear index
Higher-order nonlinearity
Ionization rate
MESA model of N2
Nonlinear index
from ab initio calculations
Metastable wavefunction
F
SAE approximation
Kolesik Group:

## Slide 24
Molecular nitrogen model: Experimental verification
Exp.
Sim.
Transverse profile at different times
Raman
Plasma
Kerr

## Slide 25
Molecular models in MESA: lessons from Nitrogen
Results so far:
Multi-electron, complex-valued Stark energy of the metastable ground state
Qualitative agreement with low-order harmonic generation
Encouraging comparison with SSSI experiments (in progress)
Next:
Other molecules, including CO2, O2
[1] J. K. Wahlstrand, Y.-H. Cheng, Y.-H. Chen, and H. M. Milchberg, Phys. Rev. Lett. 107, 103901 (2011).
[2] J. K. Wahlstrand, Y.-H. Cheng, and H. M. Milchberg, Phys. Rev. A 85, 043820 (2012).
[3] K. Y. Kim, I. Alexeev, and H. M. Milchberg, Applied Physics Letters 81, 4124 (2002).
[4] S. Zahedpour, J. K. Wahlstrand, and H. M. Milchberg, Opt. Lett. 40, 5794 (2015).
[5] J. K. Wahlstrand, S. Zahedpour, and H. M. Milchberg, J. Opt. Soc. Am. B 33, 1476 (2016).
Joint work (under Colorado MURI): A. Bahl, J.K. Wahlstrand, S. Zahedpour, H.M. Milchberg, and M. Kolesik
Nonlinear optical polarization response and plasma generation in noble gases:
Comparison of MESA models to experiments PRA, revision submitted

## Slide 26
Nonlinear HITRAN Extension for Water – First steps
K. Schuh et al., Physical Review A (accepted, Oct 2017) “Nonlinear rovibrational polarization response of water vapor to ultrashort long-wave infrared pulses”
142,000 transitions!
Cut-off criterion:
12,709
Absorption spectrum – 50 fs
Moloney, Koch, Wrigth, Kolesik
10 µm

## Slide 27: Talk Overview
Introduction
Background Theory
Developing light-matter coupling models [Task T2.2/T4.2]
Simulating 10µm Ultrashort Pulse Atmospheric Propagation [Task T3.4]
Conclusion

## Slide 28: Long Wavelength Scaling of Critical Parameters
Critical Power:
Ionized Electron Polarization
Ionized Electron Density
ground state

## Slide 29: Quantum Many-Body Equations for Coulomb Scattering
Assume ions are stationary
K. Schuh et al., PRE 88, 063102 (2013); PRE 89, 033103 (2104); PRE 93, 013208 (2016)
Requires solution of Quantum Boltzmann Equation

## Slide 30
Single and multi-electron
ionization threshold
Many-body isolated atom
K.Schuh, M. Kolesik, E.M. Wright, J.V Moloney and S.W Koch, PRL, 118 063901 February 10 (2017)
Self-Channeling of High Power LWIR Pulses in Atomic gases

## Slide 31: Many-Body Interactions of Weakly Ionized Electrons
Single Active and multi-
Electron (MESA)
M. Kolesik
Many Electron
Effective Nonlinear
Index
Effective Nonlinear
Index
Effective Nonlinear
Index
SF Threshold
800nm
4 µm
10 µm
K.Schuh, M. Kolesik, E.M. Wright, J.V Moloney and S.W Koch, PRL, 118 063901 February 10 (2017)

## Slide 32
Beam characteristics at 10 µm
240 fs pulse – filament (red dashed), 3.7cm waist, 590 mJ
1.2 ps pulse - Self-trapped whole beam self-channeling (black dashed). 3.7 cm waist, 3 J
Weak self-focusing compression beyond 1.5 km
Long Range Multi-Joule Pulse Delivery
Assumes an artificial Argon Atmosphere – remove complications of delayed nonlinearities.
Cumulative ionization (plasma) dispersion weakens effective Kerr lens
K.Schuh, M. Kolesik, E.M. Wright, J.V Moloney and S.W Koch, PRL, 118 063901 February 10 (2017)
Rayleigh range

## Slide 33: Multi-Kilometer Propagation at 10µm (no HITRAN)
Whole beam radial compression beyond 2km
Strong pulse compression in time
Fix peak power above critical
Artificial Argon atmosphere (same electronic n2 as air)
Increase energy (pulse duration)
Longer (higher energy) pulses tend to suppress strong focus but self-trap over longer ranges.
Rayleigh range

## Slide 34
Whole Beam Self-trapping

## Slide 35
Non-Gaussian Vortex Beams
D. Gordon et al Proc. SPIE Vol 9835, (2016)

## Slide 36: 10 µm Air Propagation using HITRAN Database
Pulse parameters: 3cm waist, Peak intensity 8.2x1014 Wm2, peak power = 1.14 TW – Optics Letts. 42, 3722 (2017)

## Slide 37: Talk Overview
Introduction
Background Theory
Developing light-matter coupling models [Task T2.2/T4.2]
Simulating 10µm Ultrashort Pulse Atmospheric Propagation [Task T3.4]
Conclusion

## Slide 38: Future Challenges and Research Goals
UPPE currently limited to radial symmetry for multi-km runs – almost ideal parallel scaling)
- 3D+1 simulations takes months on dedicated UV2000 system
(needed to study aberrations on exit beam)
- build in rigorously computed nonlinear responses as sources.
- DURIP proposal submitted – new generation of SGI hardware
Build a nonlinear HITRAN database for LWIR transmission windows
Extend UPPE to address scattering from remote targets
– hybrid UPPE-Maxwell solver (large angle scattering/transmission, excite evanescent waves at surfaces, etc
- implement bidirectional pulse propagator (BPPE) originally proposed in 2004.
Extend MESA quantum first principles scheme to calculate nonlinear response of
constituent air molecules – N2, O2 , H2O.
- complement with DFT and ab initio quantum simulations.
Directly support AFRL/ONR USP programs through MURI interaction and direct
collaboration with AFRL team of Dr Andreas Schmidt-Sody.
Chart: Number of cores
| 12 | 24 | 48 | 96 | 192 | 384 | 0 | 400
g-UPPEcore | 12 | 23.7915 | 46.2299 | 91.1672 | 182.1678 | 358.2598
Ideal Scaling | 0 | 400
N2 wavefunction in strong field

## Slide 39: Worst Case Scenario – Ground Level Turbulence
Simple estimate for linear propagation of a 1.5 cm beam
Longer wavelength favored in through turbulence
Scintillation appears further downstream
Problem: Rayleigh range decreases strongly with wavelength
Confined beam offsets diffraction making multi-km paths feasible.

## Slide 40: Femtosecond Filamentation Science
Remote Delivery/Spectroscopy
Complexity
Coherent X-rays – 5000-th harmonic
Exotic Robust Pulses
Curved Plasma Channels
Plasma Enhanced
Radar
Plasma channels
White light
Plasma Waveguide
- HPRF/HPM