## Slide 1: A perceptually and physiologically motivated voice source model
Gang Chen, Marc Garellek, Jody Kreiman,
Bruce R. Gerratt, and Abeer Alwan
UCLA Departments of Head and Neck Surgery,
Linguistics, and Electrical Engineering
Work supported in part by NSF and NIH/NIDCD

## Slide 2: Introduction
Many source models have been proposed but few studies have attempted to systematically validate glottal source models perceptually.
  It is unclear which (if any) deviations from perfect fit between models and data have perceptual importance.
  A perceptually-adequate model would improve efficiency of synthesis of different voice qualities.

## Slide 3: Introduction (continued)
We propose a new voice source model
  Motivated by data from high-speed laryngeal videoendoscopy
  Captures perceptually-important source shape features
This model is evaluated by comparing it to four existing source models
  MSE fit
  Perceptual adequacy

## Slide 4: Perceptual motivation
Our previous perceptual work showed:
  In the time domain, the perceptual match between target and modeled tokens was best predicted by the match at the negative peak of the flow derivative.
  Fit during the opening phase also contributed significantly to the perceptual match.
  Mismatches to the opening phase resulted in a noticeable perceptual difference between the target and modeled stimuli.

## Slide 5: The Liljencrants-Fant (LF) model
But, limited flexibility at the opening phase.
Large flexibility at the negative peak of flow derivative.

## Slide 6: The proposed model - Motivations
Perceptually motivated parameters
  Models the glottal opening phase more accurately.
Motivated by shapes of glottal area waveforms extracted from laryngeal high-speed videoendoscopy.
  A combination of sinusoidal and exponential functions to model a wide range of area and flow pulse shapes.

## Slide 7: The proposed model - Definition
6 parameters in the proposed model
  4 LF model parameters
    tp, te, Ee, and ta
  2 new parameters to provide flexibility in fitting the opening phase
    Time of the positive peak (ti)
    The shape of the opening (S1; amplitude of the waveform at ti/2)

## Slide 8: The proposed model - Equations
3 segments of definition

## Slide 9: Method: Stimuli
40 natural voice samples (20 M, 20 F)
Source estimated by inverse filtering combined with analysis-by-synthesis (AbS).
  UCLA synthesizer
  All parameters were adjusted interactively
Each estimated (target) source function was least-squares fit with 5 source models:
  The Liljencrants-Fant (LF) model
  The Rosenberg trigonometric model (Ros)
  2 models previsouly proposed by Chen, Shue, and Alwan (EE1, EE2).
  The proposed model

## Slide 10: Fitting to the landmarks
The proposed model was fitted a second time to the AbS source function with the constraint of exactly matching:
  The first point
  The positive peak of the flow derivative
  The time of maximum flow (zero-crossing of flow derivative)
  The negative peak of the flow derivative.
This procedure was included to assess the perceptual importance of the landmarks vs. the overall pulse shape.

## Slide 11: The proposed model – Fit to targets
Target AbS source pulses and the corresponding least-MSE-fitted sources using the proposed model for six different speakers. Panels (a), (b), and (c): male speakers. Panels (d), (e), and (f): female speakers. Solid line: AbS source. Dashed line: the proposed model.
The proposed model is able to approximate a wide range of pulse widths, pulse skewnesses, and abruptnesses of glottal closure.

## Slide 12: Model fitting results
MSE values (in %) between models and the target AbS sources.
“Proposed” denotes fitting the proposed model subject to MSE criteria. “Proposed-LM” denotes fitting the proposed model subject to MSE criteria with the constraint of exact landmark matching.
 | Ros | LF | EE1 | EE2 | Proposed | Proposed-LM
Male | 27.8 | 14.1 | 25.8 | 21.6 | 3.9 | 6.9
Female | 11.3 | 3.6 | 3.8 | 3.5 | 1.2 | 1.6

## Slide 13: Perceptual experiment - method
40 listeners
Stimuli synthesized with each modeled source
All other parameters held constant
A visual sort-and-rate task
  Listeners assessed the extent of perceived match between the original voice samples and each “modeled” copy.
EE1
EE2
LF
Proposed-LM
AbS
Ros
Audio samples

## Slide 14: Sort and rate task
Listeners saw icons without labels
  Place perceptually similar sounds close together
  Place dissimilar sounds farther away.
We then calculated the distance of each modeled token from the target AbS voice

## Slide 15: Perceptual experiment - results
The proposed model formed a significantly better match to the target AbS stimulus (lower mean perceptual distance) than the other models.
Normalized perceptual distances (range from 0 to 1) between the model-fitted voices and the target AbS voice. A smaller number indicates a better match to the target AbS voice.
 | Ros | LF | EE1 | EE2 | Proposed-LM
Male | 0.57 | 0.46 | 0.38 | 0.40 | 0.26
Female | 0.71 | 0.42 | 0.46 | 0.43 | 0.32

## Slide 16: Discussion and summary
Compared to the 4-parameter LF model, 2 perceptually-motivated parameters were added in the proposed model to provide more flexibility in matching the glottal opening phase.
With the increased number of parameters, it is not surprising that the proposed model provided a better model fit in MSE terms.
Nevertheless, the significant improvement in perceptual fit indicated that the source variability during the opening phase (captured by the two additional parameters) is perceptually salient.

## Slide 17: Future work
Future work will examine the effect of using this model in synthesizing continuous speech.

## Slide 18: Thank you!