## Slide 1: Roadmap
Background: Decoupled Spatial Architectures
Decoupled-Spatial Architecture Programming
Compiling High-Level- Lang. to DSA
Advanced DSA Programming
Composing a Spatial Architecture
  The Scala Embedded DSL

## Slide 2: Hardware Stack: Composing Spatial Architecture
Overview of DSAGEN H/W Stack (3 mins)
Goal: Build Your Own Spatial Architecture (25 mins)
  A Scala Embedded DSL – Build A Simple CGRA (10 mins)
  Generate IR/RTL (3 mins)💻
  Power/Area Estimation (2 mins)💻
  Build your own CGRA (10 mins)💻
Advanced Hardware Features (5 mins)
A End-to-End Approach (5 mins)
Q & A

## Slide 3: DSAGEN Hardware Stack
Define your own architecture.
  Generate the IR for compiler
  Generate the RTL for hardware research
  Design-Space Exploration
ChipYard Integration
  Run Stream-Dataflow Program Binary on DSAGEN
  Integrate with other IPs
1
2
3
4
1
2
3
4*
  *Design-Space Exploration will not be covered today

## Slide 4: Hardware Stack: Composing Spatial Architecture
Overview of DSAGEN H/W Stack (3 mins)
Goal: Build Your Own Spatial Architecture (25 mins)
  A Scala Embedded DSL – Build A Simple CGRA (10 mins)
  Generate IR/RTL (3 mins)💻
  Power/Area Estimation (2 mins)💻
  Build your own CGRA (10 mins)💻
Advanced Hardware Features (5 mins)
A End-to-End Approach (5 mins)
Q & A

## Slide 5: A Scala Embedded DSL – Build A Simple CGRA
Our Spatial Architecture:
  CGRA
    Processing Element
    Switch
    Vector Port
  Memory System
  RISC-V CPU (Rocket Core)
RISCV CPU
Memory
Mem. Controller
＋
a[0:n]
c[0:n]
b[0:n]
Recurrence

## Slide 6: A Scala Embedded DSL – Build A Simple CGRA

## Slide 7: A Scala Embedded DSL – Build A Simple CGRA
val vport_i1 = new ssnode("vector port")
val vport_i2 = new ssnode("vector port")
val vport_o1 = new ssnode("vector port")
vport_o1
vport_i2
vport_i1
val pe = new ssnode("processing element")
pe("instructions", Seq("Add", "Mul"))
val sw1 = new ssnode("switch")
val sw2 = new ssnode("switch")
val sw3 = new ssnode("switch")
val sw4 = new ssnode("switch")
sw1
sw2
sw3
sw4
pe

## Slide 8: A Scala Embedded DSL – Build A Simple CGRA
// define connection my_cgra( vport_i1 --> sw1)( vport_i2 --> sw2)( sw3 --> vport_o1)( sw1 <-> sw2)( sw1 <-> sw3)( sw2 <-> sw4)( sw3 <-> sw4)( sw1 --> pe)( sw2 --> pe)( sw3 --> pe)( sw4 <-> pe )
vport_o1
vport_i2
vport_i1
sw1
sw2
sw3
sw4
pe
// define the CGRA fabric val my_cgra = new ssfabric my_cgra("default_data_width", 64)
// define connection my_cgra( vport_i1 --> sw1)( vport_i2 --> sw2)( sw3 --> vport_o1)( sw1 <-> sw2)( sw1 <-> sw3)( sw2 <-> sw4)( sw3 <-> sw4)( sw1 --> pe)( sw2 --> pe)( sw3 --> pe)( sw4 <-> pe )
// define connection my_cgra( vport_i1 --> sw1)( vport_i2 --> sw2)( sw3 --> vport_o1)( sw1 <-> sw2)( sw1 <-> sw3)( sw2 <-> sw4)( sw3 <-> sw4)( sw1 --> pe)( sw2 --> pe)( sw3 --> pe)( sw4 <-> pe )
// define connection my_cgra( vport_i1 --> sw1)( vport_i2 --> sw2)( sw3 --> vport_o1)( sw1 <-> sw2)( sw1 <-> sw3)( sw2 <-> sw4)( sw3 <-> sw4)( sw1 --> pe)( sw2 --> pe)( sw3 --> pe)( sw4 <-> pe )

## Slide 9: A Scala Embedded DSL – Build A Simple CGRA
vport_o1
vport_i2
vport_i1
sw1
sw2
sw3
sw4
pe
// dsa-cgra-gen/src/main/real/micro_demo
package real import dsl._ object micro_demo extends App{ // define vector port val vport_i1 = new ssnode("vector port") val vport_i2 = new ssnode("vector port") val vport_o1 = new ssnode("vector port") // define switch val sw1 = new ssnode("switch") val sw2 = new ssnode("switch") val sw3 = new ssnode("switch") val sw4 = new ssnode("switch") // define processing element that can do Add and Mul val pe = new ssnode("processing element") pe("instructions", Seq("Add", "Mul")) // define the CGRA fabric val my_cgra = new ssfabric my_gra("default_data_width", 64) // define connection my_cgra( vport_i1 --> sw1)(vport_i2 --> sw2)( sw3 --> vport_o1)( sw1 <-> sw2)(sw1 <-> sw3)(sw2 <-> sw4)(sw3 <-> sw4)( sw1 --> pe)(sw2 --> pe)(sw3 --> pe)(sw4 <-> pe ) }

## Slide 10: Hardware Stack: Composing Spatial Architecture
Overview of DSAGEN H/W Stack (3 mins)
Goal: Build Your Own Spatial Architecture (25 mins)
  A Scala Embedded DSL – Build A Simple CGRA (10 mins)
  Generate IR/RTL (3 mins)💻
  Power/Area Estimation (2 mins)💻
  Build your own CGRA (10 mins)💻
Advanced Hardware Features (5 mins)
A End-to-End Approach (5 mins)
Q & A

## Slide 11: Before we start...
Tool(s) I will use: ss_sched (in dsa-release.zip)
Repositories: dsa-framework/dsa-cgra-gen, dsa-examples
  dsa-framework/dsa-cgra-gen
$ cd <you workspace>
$ git clone https://github.com/PolyArch/dsa-framework.git
$ cd dsa-framework
$ git submodule update --init dsa-cgra-gen
  dsa-examples
  $ cd <you workspace>
  $ git clone https://github.com/PolyArch/dsa-examples.git
Optional Tools:
  Graphviz:
  $ sudo apt-get install graphviz

## Slide 12: Generate IR/RTL 💻
// dsa-cgra-gen/src/main/real/micro_demo
package real import dsl._ object micro_demo extends App{ // define vector port ………… // define switch ………… // define processing element that can do Add and Mul ………… // define the CGRA fabric ………… // define connection …………
// print IR my_cgra.printIR(filename = "my_cgra") }
1. Add printIR to the end of CGRA description file
2. Generate IR through sbt
$ cd dsa-framework/dsa-cgra-gen
$ sbt
$ sbt:dsa-cgra-gen> runMain real.micro_demo
3. Check the generated IR
// dsa-cgra-gen/my_cgra.json
{ "default_data_width" : 64, "identifier" : [ "id", "nodeType" ],
.........
"module_type" :"cgra.fabric.cgra_fabric" }
4. Generate RTL (Verilog)
$ cd dsa-framework/dsa-cgra-gen && sbt
$ sbt:dsa-cgra-gen>
cgra.driver.generator my_cgra.json

## Slide 13: Hardware Stack: Composing Spatial Architecture
Overview of DSAGEN H/W Stack (3 mins)
Goal: Build Your Own Spatial Architecture (25 mins)
  A Scala Embedded DSL – Build A Simple CGRA (10 mins)
  Generate IR/RTL (3 mins)💻
  Power/Area Estimation (2 mins)💻
  Build your own CGRA (10 mins)💻
Advanced Hardware Features (5 mins)
A End-to-End Approach (5 mins)
Q & A

## Slide 14: Power/Ares Estimation💻
1. Power and Area Estimation is done via spatial scheduler
$ cp dsa-framework/dsa-cgra-gen/my_cgra.json
dsa-examples/hw
$ cd dsa-examples/hw
$ ss_sched my_cgra.json
--------- Sample Results like below ---------
FU: 422075um2 447.399mw
Network: 91593um2 22.8983mw
Sync: 139971um2 96.2mw
Memory: 39325um2 12.14mw
--------- What’s your result ? ---------
2. Power/Area Estimation Results via Spatial-Scheduler

## Slide 15: Hardware Stack: Composing Spatial Architecture
Overview of DSAGEN H/W Stack (3 mins)
Goal: Build Your Own Spatial Architecture (25 mins)
  A Scala Embedded DSL – Build A Simple CGRA (10 mins)
  Generate IR/RTL (3 mins)💻
  Power/Area Estimation (2 mins)💻
  Build your own CGRA (10 mins)💻
Advanced Hardware Features (5 mins)
A End-to-End Approach (5 mins)
Q & A (2 mins)

## Slide 16: Build Your Own CGRA 💻
vport_o1
vport_i2
vport_i1
sw1
sw2
sw3
sw4
Add/
Mul
vport_i3
sw5
Div
Can you build a CGRA like this?
// dsa-cgra-gen/src/main/scala/real/micro_demo_answer
package real import dsl._ object micro_demo_sihao extends App{ .......
// put your code here
  // Add a new vector port val vport_i3 = new ssnode("vector port") // Add a new switch val new_sw = new ssnode(“switch") // Add a new processing element val pe_div = new ssnode("processing element") pe_div("instructions", Seq(“UDiv")) // Add connections to fabric my_cgra(vport_i3 --> new_sw)( sw1 --> pe_div)( new_sw --> pe_div)( pe_div --> sw3)
// print IR my_cgra.printIR(filename = "my_cgra_div") }
Answer:

## Slide 17: Visualize Your Own CGRA 💻
Perform spatial schedule
$ cd <your workspace>/dsa-examples/hw
$ ss_sched my_cgra_div.json add-div.dfg
Visualize the schedule result (graphviz required)
$ cd <your workspace>/dsa-examples/hw/viz
$ neato -Goverlap=false -Gstart=self -Gepsilon=.0000001 -Tpng -o \
add-div_my-cgra.png ./add-div.my_cgra_div.gv

## Slide 18: Visualize Your Own CGRA 💻

## Slide 19: Hardware Stack: Composing Spatial Architecture
Overview of DSAGEN H/W Stack (3 mins)
Goal: Build Your Own Spatial Architecture (25 mins)
  A Scala Embedded DSL – Build A Simple CGRA (10 mins)
  Generate IR/RTL (3 mins)💻
  Power/Area Estimation (2 mins)💻
  Build your own CGRA (10 mins)💻
Advanced Hardware Features (5 mins)
A End-to-End Approach (5 mins)
Q & A (2 mins)

## Slide 20: Basic Concept: Switch
Simplest Switch
4 Input Ports
3 Output Ports
1 9-bit Config. Register
  For each output, we need 3 bit to specify 5 inputs (Input 1~4 + Ground) x 3 Outputs = 9-bit config
Decode config. information
A 4-Input 3-Output Switch
Config.
// Define Switch val my_sw = new ssnode("switch")
Simplest Switch
MUX
MUX
MUX

## Slide 21: Basic Concept: Processing Element
The number of operand is decided by ALU, which will affect the width of config. file
Hardware should be reused if some operations are subset of a bigger operation (like ADD16x4 and ADD64)
Function
Unit
Instruction Buffer
Instruction Scheduler
Register
File
MUX
MUX
// Define Your Processing Elements with Add / Sub / Mul val my_fu = new ssnode(“processing elements") my_fu( "instructions",Seq("Add", "Sub", "Mul"))( "data_width", 64)

## Slide 22: Basic Concept: Decomposability
16
16
16
16
16
16
16
16
16
16
16
16
Example DFG
Mul16
16
16
A
B
Mul16
16
16
C
D
Cat16
32
Hardware Support
PE
Mul 16
16
16
16
16
valid
invalid
invalid
invalid
16
16
16
16
valid
invalid
invalid
invalid
PE
Mul 16
16
16
16
16
valid
invalid
invalid
invalid
16
16
16
16
valid
invalid
invalid
invalid
PE
Cat 16
16
16
16
16
red means data is valid
16
16
16
16
32
32
here:
we shift data by 16-bit
here:
we keep data at its original place

## Slide 23: Advanced Features: Decomposability in Switch
A 4-Input 3-Output Switch
Define Decomposable Switch
Config.
// Define Decomposable Switch val my_switch = new ssnode("switch") my_switch( "data_width", 64)( "granularity",16)( "subnet_offset", Seq(0, 1, 2))
subnet_offset = 1
0x1234__5678__9abc__de01
0x5678__9abc__de01__1234
subnet_offset = 2
0x1234__5678__9abc__de01
0x9abc__de01__1234__5678
Sub-net Shifter Offset
In order to achieve decomposability, we add one subnet shifters for each output
The default offset is zero for each output
MUX
MUX
MUX

## Slide 24: Advanced Features: Decomposability in PE
All you need to do is just changing the granularity from 64 to 32.
// Define Your own Data-dependent Controlled // Processing Elements with GE / LE and Add val my_fu = new ssnode(“processing element") my_fu( "instructions",Seq(“Add"))( "data_width", 64)(
// Here we decompose the processing elements "granularity", 32)
"granularity", 64
"granularity", 32

## Slide 25: Advanced Features: Dynamic Flow Control
In order to build dynamic switch, we need to add a Queue for every output.
For every IO port, two more wires (Valid/Ready) are added to implement backpressure.
A 4In-3Out Decomposable Dynamic Switch
// Define Decomposable Dynamic Switch val my_switch = new ssnode("switch") my_switch( "data_width", 64)( "granularity",16)( "flow_control", true )
Define Decomposable Dynamic Switch
MUX
Conf.
Valid/Ready
Valid/Ready
Valid/Ready
Valid/Ready
Valid/Ready
Valid/Ready
Valid/Ready
MUX
MUX
Notes: A better transition
The overview of the properties of the modules.
I need to convey the hardware feature -> software mapping. Different hardware feature has different cost, and hw and sw feature cost wil result into different overall performance
Tell the people the why to have the different modules, we don’t force each processing elements to have all features. Flow control:
1. we talk about the feature Vidushi talked about the backpressure, and what is the cost add the feature to different processing element and switch and make the switch to do that work

## Slide 26: Advanced Features: Data-Controlled
A data-dependent controlled processing element is created based on its `instructions` field
Self-Control (`SelfCtrl`) instructions will use its own computed result to access CLT
Input-Control (`InputCtrl`) instruction will use the input from upstream to access CLT
discard
Func. Unit
ACC
CLT
FIFO0
FIFO1
FIFO2
Data-dependent Control
Processing Element
reuse
reset
NE
NW
SE
SW
NE
NW
SE
SW
NE
NW
SE
SW
SE
Stream-Join
Flow-Ctrl
Data-Flow
// Define Your own Data-dependent Controlled // Processing Elements with GE / LE and Add val my_fu = new ssnode(“processing elements") my_fu( "instructions",Seq("SelfCtrlGE", "SelfCtrlLE", "InputCtrlMin"))( "data_width", 64)

## Slide 27: Advanced Features: Mesh Topology
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
ID is by default to identify a node, but you can add more identifier.
Like for mesh topology, natural identifiers will be the `column index` and `row index`.
// Keys that differ nodes identifier("row_idx","col_idx")
// Building a 5 x 5 processing elements array val peArray = Array( Array(pe_spc, pe_add, pe_add, pe_add, pe_spc), Array(pe_spc, pe_add, pe_add, pe_add, pe_spc), Array(pe_add, pe_add, pe_add, another_pe, pe_add), Array(pe_add, pe_add, another_ pe, pe_add, pe_spc),
Array(pe_add, pe_add, pe_add, another_pe, pe_add), )

## Slide 28: Advanced Features: Hardware/Software Tradeoff
Compare the Hardware Tradeoff of different delay FIFO depth
// Input FIFO (depth = 4)
.........
FU: 4990.85um2 5.23123mw
Network: 1891.03um2 0.472758mw
Sync: 5238um2 3.6mw
Memory: 39325um2 12.14mw
// Input FIFO (depth = 16)
.........
FU: 4990.85um2 5.23123mw
Network: 1891.03um2 0.472758mw
Sync: 8730um2 6mw
Memory: 39325um2 12.14mw
-> % ss_sched my_cgra_delay_depth_4.json
-> % ss_sched my_cgra_delay_depth_16.json

## Slide 29: Hardware Stack: Composing Spatial Architecture
Overview of DSAGEN H/W Stack (3 mins)
Goal: Build Your Own Spatial Architecture (25 mins)
  A Scala Embedded DSL – Build A Simple CGRA (10 mins)
  Generate IR/RTL (3 mins)💻
  Power/Area Estimation (2 mins)💻
  Build your own CGRA (10 mins)💻
Advanced Hardware Features (5 mins)
A End-to-End Approach (5 mins)
Q & A (2 mins)

## Slide 30: A End-to-End Approach💻
Add DSAGEN Hardware Generator (dsa-cgra-gen) into ChipYard
Notice: ss-chipyard (we have not released it in dsa-framework yet) has been integrated with dsa-cgra-gen
class SSCgraConfig extends Config( new chipyard.iobinders.WithUARTAdapter ++ new chipyard.iobinders.WithTieOffInterrupts ++ new chipyard.iobinders.WithBlackBoxSimMem ++ new chipyard.iobinders.WithTiedOffDebug ++ new chipyard.iobinders.WithSimSerial ++ new testchipip.WithTSI ++ new chipyard.config.WithBootROM ++ new chipyard.config.WithUART ++ new chipyard.config.WithL2TLBs(1024) ++ new freechips.rocketchip.subsystem.WithNoMMIOPort ++ new freechips.rocketchip.subsystem.WithNoSlavePort ++ new freechips.rocketchip.subsystem.WithInclusiveCache ++ new ss_cgra_gen.WithSsCgra ++ // mixed with Stream-Dataflow CGRA
new freechips.rocketchip.subsystem.WithNExtTopInterrupts(0) ++ new freechips.rocketchip.subsystem.WithNBigCores(1) ++ new freechips.rocketchip.subsystem.WithCoherentBusTopology ++ new freechips.rocketchip.system.BaseConfig )

## Slide 31: A End-to-End Approach💻
Generate the binary from C program with Stream-Dataflow Instruction
Notice: ss-chipyard (we have not released it in dsa-framework yet) has been integrated with dsa-cgra-gen
$ riscv64-unknown-elf-gcc -fno-common -fno-builtin-printf -specs=htif_nano.specs -o vec_add-ss.dsa-gnu.o -c vec_add-ss.cc
$ riscv64-unknown-elf-gcc -static -specs=htif_nano.specs vec_add-ss.dsa-gnu.o -o vec_add-ss.cy-gnu.riscv
Link kernel via chipyard riscv-toolchain
$ make run-binary-debug SUB_PROJECT=ss_cgra_gen BINARY=<dir to binary>/vec_add-ss.cy-gnu.riscv
Run binary program on hardware simulator (verilator)

## Slide 32: Hardware Stack: Composing Spatial Architecture
Overview of DSAGEN H/W Stack (3 mins)
Goal: Build Your Own Spatial Architecture (25 mins)
  A Scala Embedded DSL – Build A Simple CGRA (10 mins)
  Generate IR/RTL (3 mins)💻
  Power/Area Estimation (2 mins)💻
  Build your own CGRA (10 mins)💻
Advanced Hardware Features (5 mins)
A End-to-End Approach (5 mins)
Q & A (2 mins) Any questions?

## Slide 33: Advanced Features: Customized Connection
sw
sw
sw
sw
PE
1
2
3
4
for(row_idx <- 0 until 5;col_idx <- 0 until 5){
// Pick out the processing elements from pe array val temp_node = peArray(row_idx)(col_idx).clone
// assign the identifier pe_node("row_idx",row_idx)("col_idx",col_idx) dev( dev(row_idx)(col_idx)("switch") --> pe_node )( dev(row_idx+1)(col_idx)("switch") --> pe_node )( dev(row_idx)(col_idx+1)("switch") --> pe_node )( dev(row_idx+1)(col_idx+1)("switch") <-> pe_node ) }
1
2
3
4
Pick out a node from fabric
Build Connection
val net : ssfabric
val node : ssnode =
net(“key”, value)
val node1 : ssnode
val node2 : ssnode
val link1 : sslink = node1 --> node2 // connection from left to right
val link2 : sslink = node1 <-- node2 // connection from right to left
val link3 : sslink = node1 <-> node2 // dual-direction connection