## Slide 1: DSAGEN: Democratizing the Research on Spatial Accelerators
Jian Weng, Sihao Liu, Vidushi Dadu, Tony Nowatzki
University of California, Los Angeles
Oct. 17th, 2020

## Slide 2: Roadmap
Background: Decoupled Spatial Architectures
Hands-on Exercises
  Basics of Decoupled-Spatial Architecture Infra
  Advanced DSA Programming
  Compiling High-Level Lang. to DSA
    Pragma Annotated Compilation
      Why pragma’s?
    Example 1: Vector Add
    Modular Compilation with Examples
  Composing a Spatial Architecture

## Slide 3: Compiling High-Level Lang. to Decoupled Spatial
Programmer Hints
  Which code regions are offloaded onto the spatial accelerator?
  Which memory accesses can be decoupled intrinsics?
  Which offloaded regions should be concurrent?
Executable Binary
Apps
?
How to abstract diverse underlying features with a unified high-level interface?
Pragma Annotation
Notes: We have a wide design space, so our programming language needs to be generic enough. This means a DSL, like Halide or TF, does not suffice.
Instead we adopt C.
The key challenge to overcome is how to have a unified high-level interface to abstract the diverse underlying hardware.
In order to do this without massive compiler effort, we rely on programmers to provide these hints.

## Slide 4: Roadmap
Background: Decoupled Spatial Architectures
Hands-on Exercises
  Basics of Decoupled-Spatial Architecture Infra
  Advanced DSA Programming
  Compiling High-Level Lang. to DSA
    Pragma Annotated Compilation
    Example 1: Vector Add
      An exemplified pragma’s annotation!
    Modular Compilation with Examples
  Composing a Spatial Architecture

## Slide 5: Pragmas --- Which to Offload?
#pragma ss dfg [temporal] [unroll(x)]
  Annotate either a loop or a compound body
  Enable temporal if you want to offload onto shared Pes
  Enable unroll if you want to occupy more FU resources
// vanilla code
for (int i = 0; i < n; ++i)
c[i] = a[i] + b[i];
#pragma ss dfg unroll(4)
for (int i = 0; i < n; ++i)
c[i] = a[i] + b[i];

## Slide 6: Pragmas --- What to Decouple?
#pragma ss stream [nonblock]
  Annotate a loop
  Hints that the memory access below are restrict
  Enable the clause if you do not want to inject SS_WAIT_ALL to sync after this region is done
#pragma ss stream
#pragma ss dfg unroll(4)
for (int i = 0; i < n; ++i)
c[i] = a[i] + b[i];
#pragma ss dfg unroll(4)
for (int i = 0; i < n; ++i)
c[i] = a[i] + b[i];

## Slide 7: Pragmas --- What to be concurrent?
#pragma ss config
  Annotate a compound body
  The #pragma ss dfg in this body will be concurrent on the spatial architecture
#pragma ss stream
#pragma ss dfg unroll(4)
for (int i = 0; i < n; ++i)
c[i] = a[i] + b[i];
#pragma config
{
#pragma ss stream
#pragma ss dfg unroll(4)
for (int i = 0; i < n; ++i)
c[i] = a[i] + b[i];
}

## Slide 8: Example 1: Vector Add (Pragma Compilation)
// compile/main.cc
#pragma config
{
#pragma ss stream
#pragma ss dfg unroll(4)
for (int i = 0; i < n; ++i)
c[i] = a[i] + b[i];
}
Modified clang
main.bc
DSA Xform Pass
dsa-main.bc
DFG’s
Generic Opt.
O3-dsa-main.bc
Code Select
O3-dsa-main.s
GNU Linker
O3-dsa-main.out
$ ./run.sh O3-dsa-main.out
$ ./run.sh main.out
Notes: To program an accelerator with such programming paradigm, we need to decouple the computation and memory accesses in order to map them to the corresponding hardware component.
The computations are represented in a data dependence graph and mapped onto a spatial architecture which consist of PEs for performing computations and switches for routing the dependences.
The memory access are encoded in control intrinsics issued from the control host to the memory controller. Then the memory controller sends memory request so that the data can stream through the spatial architecture to execute the program.
When multiple data streams need to be synchronized, a sync. elem. made of coordinating FIFOs will ensure a proper timing.
I will discuss the design tradeoffs of the key hardware primitives in the next a few slides.

## Slide 9: Decoupled-Spatial Xform
// compile/main.cc
#pragma config
{
#pragma ss stream
#pragma ss dfg unroll(4)
for (int i = 0; i < n; ++i)
c[i] = a[i] + b[i];
}
# compile/main.bc
%0 = call ss.config.begin()
i = 0
loop:
%1 = load a[i]
%2 = load b[i]
%3 = add %1, %2
store c[i], %2
i += 1
br i < n, loop !0
%4 = call ss.config.end(%0)
!0 = {"ss.dfg", 4, !1}
!1 = {"ss.stream"}
❶
❷
⓿ Config scopes are guarded by intrinsic functions
❶ Loop hints are encoded in metadata
❷ Starting with memory loads and ending with memory store, traverse the dependence graph to decouple them. Memory instructions will be analyzed and encoded in control cmd.
❸ Decoupled computational instructions are duplicated by the unrolling degree and fed to the spatial compiler.
❸
⓿
Clang Compiler

## Slide 10: Decoupled-Spatial Xform
# compile/main.bc
%0 = call ss.config.begin()
i = 0
loop:
%1 = load a[i]
%2 = load b[i]
%3 = add %1, %2
store c[i], %2
i += 1
br i < n, loop !0
%4 = call ss.config.end(%0)
!0 = {"ss.dfg", 4, !1}
!1 = {"ss.stream"}
Input: sub0_1[4]
Input: sub0_2[4]
sub0_30 = Add64(sub0_10, sub0_20)
sub0_31 = Add64(sub0_11, sub0_21)
sub0_32 = Add64(sub0_12, sub0_22)
sub0_33 = Add64(sub0_13, sub0_23)
Output: sub0_3[4]
SS_CONFIG(X_config, X_size)
SS_LINEAR_READ(a, 8*n, P_X_sub0_1)
SS_LINEAR_READ(b, 8*n, P_X_sub0_2)
SS_LINEAR_WRITE(P_X_sub0_3, a, 8*n)
i = 0
loop:
i += 1
br i<n, loop !0
SS_WAIT_ALL()
!0 = {"ss.dfg", 4, !1}
!1 = {"ss.stream"}
This loop will be eliminated when generic optimization

## Slide 11: Example 2: Vector Normalization (Compilation)
acc = 0.0; for (int i = 0; i < N; ++i) acc += a[i] * a[i]; norm = 1.0 / sqrt(acc); for (int i = 0; i < N; ++i) a[i] = a[i] * norm;
acc = 0.0;
#pragma ss stream
#pragma ss dfg for (int i = 0; i < N; ++i) acc += a[i] * a[i];

## Slide 12: Example 2: Vector Normalization (CONT’D)
acc = 0.0; for (int i = 0; i < N; ++i) acc += a[i] * a[i]; norm = 1.0 / sqrt(acc); for (int i = 0; i < N; ++i) a[i] = a[i] * norm;
acc = 0.0;
#pragma ss stream nonblock
#pragma ss dfg for (int i = 0; i < N; ++i) acc += a[i] * a[i];
#pragma ss dfg temporal
{ norm = 1.0 / sqrt(acc);
}
nonblock: Since the result of the accumulation region is forward to the scalar region, we do not want to sync the first region.

## Slide 13: Example 2: Vector Normalization (CONT’D)
acc = 0.0; for (int i = 0; i < N; ++i) acc += a[i] * a[i]; norm = 1.0 / sqrt(norm); for (int i = 0; i < N; ++i) a[i] = a[i] * norm;
double acc = 0.0;
#pragma ss stream nonblock
#pragma ss dfg for (int i = 0; i < N; ++i) acc += a[i] * a[i];
#pragma ss dfg temporal
{ norm = 1.0 / sqrt(acc);
}
#pragma ss stream
#pragma ss dfg for (int i = 0; i < N; ++i) a[i] = a[i] * norm;

## Slide 14: Example 2: Vector Normalization (CONT’D)
acc = 0.0; for (int i = 0; i < N; ++i) acc += a[i] * a[i]; norm = 1.0 / sqrt(norm); for (int i = 0; i < N; ++i) a[i] = a[i] * norm;
#pragma ss config
{
double acc = 0.0;
#pragma ss stream nonblock
#pragma ss dfg for (int i = 0; i < N; ++i) acc += a[i] * a[i];
#pragma ss dfg temporal
{ norm = 1.0 / sqrt(acc);
}
#pragma ss stream
#pragma ss dfg for (int i = 0; i < N; ++i) a[i] = a[i] * norm;
}

## Slide 15: ./run.sh O3-dsa-main.out
Simulator Time: 0.01652 sec Cycles: 275 Number of coalesced SPU requests: 0 Control Core Insts Issued: 38 Control Core Discarded Insts Issued: 27 Control Core Discarded Inst Stalls: 0.7105 Control Core Config Stalls: 0.05091 Control Core Wait Stalls: 0.9127 (ALL) ACCEL 0 STATS *** Commands Issued: 6 CGRA Instances: 130 -- Activity Ratio: 0.9382, DFGs / Cycle: 0.4727 For backcgra, Average thoughput of all ports (overall): 0.1576, CGRA outputs/cgra busy cycles: 0.5 039 CGRA Insts / Computation Instance: 2.969

## Slide 16: Modular Compilation
By default, the compiler assumes all the features are enabled.
When disabled, a fallback transformation escapes this feature is invoked.
  TEMPORAL Processing Elements --- 02_vector_norm
  RECcurrence Bus --- 03_gemm.cc
  INDirect Memory --- 04_crs.cc
Use these bold words environment variable to 0 to disable the corresponding feature and try the workloads.

## Slide 17: TEMPORAL=0 ./run.sh O3-dsa-main.out
Simulator Time: 0.02559 sec Cycles: 1691 Number of coalesced SPU requests: 0 Control Core Insts Issued: 880 Control Core Discarded Insts Issued: 115 Control Core Discarded Inst Stalls: 0.1307 Control Core Config Stalls: 0.008279 Control Core Wait Stalls: 0.07629 (ALL) ACCEL 0 STATS *** Commands Issued: 5 CGRA Instances: 129 -- Activity Ratio: 0.152, DFGs / Cycle: 0.07629 For backcgra, Average thoughput of all ports (overall): 0.03814, CGRA outputs/cgra busy cycles: 0. 5019 CGRA Insts / Computation Instance: 2.977 CGRA Insts / Cycle: 0.2271 (overall activity factor)