## Slide 1: Roadmap
Background: Decoupled Spatial Architectures
Hands-on Exercises
  Decoupled-Spatial Architecture Programming
  Advanced DSA Programming
  Composing a Spatial Architecture
  DSAGEN for your Research
    Adding a New Instruction Capability to Processing Elements
      Overview: The Organization of Spatial Schedule
      Integrate the Instruction
    Adding a New Host Control Command

## Slide 2: Our Goal: Adding an Instruction Capability to Spatial Processing Elements
Mixed precision instruction is a newly emerging idiom in many general-purpose processors
Give our spatial PEs the capability of this instruction
// ARM SDOT.i8.v64
int32_t c[2];
int8_t a[8], b[8];
for (i=0; i<2; ++i) {
for (j=0; j<4; ++j) {
int32_t A = (int32_t)a[i*4+j];
int32_t B = (int32_t)b[i*4+j];
c[i] += A * B;
}
}

## Slide 3: A Brief Codebase Walk Through (Spatial Scheduler)
src/arch/*: Data structures for hardware description.
src/dfg/*: Data structures for parsed dataflow graph.
Dataflow graph simulation.
src/mapper/*: Strategies for adjusting the spatial mapping.
src/schedule/*: Data structures that records spatial mapping
src/insts/*: Instruction enum, information (II, lat, power, area, and etc.), and behavior simulation.
drivers/*: The drivers of scheduler and design space explorer.
Automatically generate
  The registered instruction enum
  Integrate the instruction behavior for simulation
  Helper functions getting the information

## Slide 4: Add a New PE Instruction
src/insts/inst_model.cpp: the implementation of an instruction integration generator, which generates:
  The enum of each instruction.
  A function that dispatches enum to simulation behaviors.
  Helper functions that returns the information of each instruction:
    II, name, latency, and num of operands/outputs
./inst_model [index of instructions] [power/area] [output header] [output cxx]
  Index of Instructions: ssinst.full
  Power/area information gathered from synthesis
  Output Header/CXX: The name of the output files.

## Slide 5: What instructions are available on the spatial accelerator?
src/insts/full.ssinst: The metadata of each instruction.
How do I extend my instructions?
#Instruction Bitwidth NumOperands OutputValues Latency II
Add64 64 2 1 2 1
src/insts/inst_model.cpp: The instruction metadata generator.
./inst_model [index of instructions] [power/area] [output header] [output cxx]
  Use src/insts/full.ssinst as index to gather affiliated metadata of each instruction, including power, area, and simulation behavior.
// Return the first output
uint64_t execute(
std::vector<uint64_t> &ops, // Operands
std::vector<uint64_t> &outs, // Other outputs
std::vector<uint64_t> &regs, // Register File
std::vector<uint64_t> &discard, // Data Predicate
std::vector<uint64_t> &back_array // Backpressure
) {
return (int64_t) ops[0] + (int64_t) ops[1];
}

## Slide 6: Add a New PE Instruction (Cleanup)
Be careful about the data type casting!
It is something like “soft-float” ABI — uint64_t is actually storing the binary format of a floating-point number.
double a = (double) ops[0];
double b = (double) ops[1];
return (uint64_t) a * b;
double a = *reinterpret_cast<double*>(&ops[0]);
double b = *reinterpret_cast<double*>(&ops[1]);
double c = a * b;
return *reinterpret_cast<double*>(&c);

## Slide 7: Roadmap
Background: Decoupled Spatial Architectures
Hands-on Exercises
  Decoupled-Spatial Architecture Programming
  Advanced DSA Programming
  Composing a Spatial Architecture
  DSAGEN for your Research
    Adding a New Instruction Capability to Processing Elements
    Adding a New Host Control Command
      Overview: The sw/hw Interface and Hardware Simulator
      Adding the Instruction along with the Code Path

## Slide 8: What if we do not want to accumulate from zero?
Proposed Solution: Add a control command to modify the register file of PEs.
Software Interface:
  SS_SET_REG(inst, reg_id, value)
  Set the reg_idth register of PE to which the instruction is mapped to value.
Implement the interface:
  Binary Assembler
  Hardware Simulator
// manual/compute.dfg
Input: A
Input: S
B = FMul64(A, A)
O = FAccumulate64(B,
ctrl=S{1:d})
Output: O
----
#pragma group temporal
Input: NORM2
NORM = Sqrt(NORM2)
INV = FDiv(1.0, NORM2)
Output: INV
----
Input: V
Input: C
B = FMul64(V, C)
Output: B
ID
00
01
02
03
04
05
06
07
08
09
10
11
12

## Slide 9: Our Goal: Adding a Control Command
Change the register file in a specific PE
  It is useful when accumulating from a non-zero initial value.
Software/hardware interface:
  #define SS_REG_WRITE(inst_id, reg_id, value) \
  ss_reg_set $rs1, $rs2, imm
  Change the value of the register whose subscript is reg_id in PE to which instruction whose ID is inst_id is mapped to value.
Compiler
  Binary format, and mnemonic
Hardware Simulator
  Decode and dispatch to the accelerator
// manual/compute.dfg
Input: A
Input: S
B = FMul64(A, A)
O = FAcc64(B, S)
Output: O
----
#pragma group temporal
Input: NORM2
NORM = Sqrt(NORM2)
INV = FDiv(1.0, NORM2)
Output: INV
----
Input: V
Input: C
B = FMul64(V, C)
Output: B
id
00
01
02
03
04
05
06
07
08
09
10
11
12

## Slide 10: A Brief Codebase Walk Through (Hw/Sw Interf. & Sim.)
dsa-riscv-ext
riscv-gnu-toolchain
dsa-gem5
spatial-scheduler
dsa-binary
programs
dsa-llvm-project
arch/arch/riscv/decode.isa
src/cpu/minor/exec_context.h
src/cpu/minor/ssim/*
opcodes-dsa
riscv-dsa.c
autopatch.py
dsaintrin.h
binary format of the extended ISA
mnemonic of the extended ISA
macro intrinsic wrapper
Patch the binary assembler and of GNU toolchain.
Decode the instruction
Execute the instruction
Change the data structure of the spatial accelerator
Infra Build
Workload Compilation
Runtime Simulation

## Slide 11: Dive into the Extended ISA: Custom Slots of RISCV
#define SS_DMA_READ(addr, stride, size, n, port) \
__asm__ __volatile__("ss_dma_rd %1, %2, %3", "r"(stride), "r"(n), "i"(1)) \
__asm__ __volatile__(“ss_dma_rd %1, %2, %3”, “r”(addr), “r”(size), "i"((port)<<1))
opcode Inst[4:2] | opcode Inst[6:5] | funct3 |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
010 | 00 | cfg_port | ctx | cfg | fill_mode |  |  |  | 
010 | 01 | add_port | scr_rd | seg_reg | dma_rd | const | recv | atom_op | cfg_mmap
110 | 10 |  | wr_scr | rem_port | wr_dma | grab | wr_rd | const_scr | cfg_atopm_op
110 | 11 | stride |  | set_iter | wait_df | wait | ind | ind_wr | cfg_ind
#define SS_SET_REG(id, reg, value) \
__asm__ __volatile__("ss_set_reg %1, %2, %3", "r"(id), "r"(value), "i"(reg))

## Slide 12: A Brief Codebase Walk Through (Hw/Sw Interf. & Sim.)
dsa-riscv-ext
riscv-gnu-toolchain
dsa-binary
programs
dsa-llvm-project
opcodes-dsa
riscv-dsa.c
autopatch.py
dsaintrin.h
binary format of the extended ISA
mnemonic of the extended ISA
macro intrinsic wrapper
Infra Build
#mnemonic operands functc3 i[6:5] i[4:2] i[1:0] ss_dma_rd rs1 rs2 bimm12hi bimm12lo 14..12=3 6..5=1 4..2=2 1..0=3 # S-type
ss_set_reg rs1 rs2 bimm12hi bimm12lo 14..12=2 6..5=1 4..2=2 1..0=3 # S-type
{"ss_dma_rd", 0, INSN_CLASS_I, "s,t,q", MATCH_SS_DMA_RD, MASK_SS_DMA_RD, match_opcode, 0},
{"ss_seg_reg",0, INSN_CLASS_I, "s,t,q", MATCH_SS_DMA_RD, MASK_SS_DMA_RD, match_opcode, 0},
dsa-riscv-ext/opcodes-dsa
Binary Compilation
Patched bin-utils
dsa-riscv-ext/riscv-dsa.c
$ make dsa-riscv-ext

## Slide 13: A Brief Codebase Walk Through (Simulation)
dsa-gem5/src/cpu/minor/ssim/accel.cc
RISCV CPU
Memory
Mem. Controller
dss-gem5/src/arch/riscv/isa/decoder.isa
dsa-gem5/src/cpu/minor/exec_context.hh
dsa-gem5/src/cpu/minor/ssim/ssim.cc
spatial-scheduler/src/dfg/ssdfg.cpp
Rec Bus
Execute the streams and coordinate the interface FIFO buffer.
Execute the dataflow graph with the delay and latency information.
// dsa-gem5/src/arch/riscv/isa/decode.isa
0xa: decode FUNCT3 { // 0xa = 10 = 2^4+2
// ...
0x2: SSOp::ss_dma_rd({{ xc->pushStreamDimension(Rs1, Rs2, imm >> 1); if (~imm & 1) { xc->callSSFunc(SS_MEM_PRT);
} }}, IsSSStream, IsNonSpeculative, No_OpClass);
0x3: SSOp::ss_set_reg({{
// Pass Rs1, Rs2, Rs3 to xc state xc->callSSFunc(SS_SET_REG);
}}, IsSSStream, IsNonSpeculative, No_OpClass);
// dsa-gem5/src/cpu/minor/ isa/exec_context.hh
switch(ss_func_code) {
// ...
case SS_PRT_MEM: ssim.write_dma(); break;
case SS_SET_REG:
ssim.accel->sched->dfg->nodes[id]
->_reg[idx] = val;
break;

## Slide 14: Resources
Tutorial Website
  http://www.seas.ucla.edu/~jianw/dsagen/tutorial.html
Released Source
  https://github.com/PolyArch/dsa-framework
Binary and Docker
  On Tutorial Website
Hands-on Exercises
  https://github.com/PolyArch/dsa-examples
Related Papers
  Jian Weng=, Sihao Liu=, Vidushi Dadu, Zhengrong Wang, Tony Nowatzki, “DSAGEN: Synthesizing Programmable Spatial Architectures”, ISCA 2020
  Jian Weng, Sihao Liu, Zhengrong Wang, Vudushi Dadu, Tony Nowatzki, “A Hybrid Systolic-Dataflow Architecture for Inductive Matrix Algorithms”, HPCA 2020
  Vidushi Dadu, Jian Weng, Sihao Liu, Tony Nowatzki, “Toward General Purpose Acceleration by Exploiting Common Data-Dependence Forms”, MICRO 2019