## Slide 1: A Hybrid Systolic-Dataflow Architecture for Inductive Matrix Algorithms
Jian Weng, Sihao Liu, Zhengrong Wang, Vidushi Dadu, Tony Nowatzki
University of California, Los Angeles
Feb 27th, 2020
Notes: Good afternoon everyone, this is Jian Weng, a third-year PhD student from UCLA.
Welcome to the presentation of our paper “A Hybrid Systolic Dataflow Architecture for Inductive Matrix Algorithms”.
Motivated by the oncoming proliferation of the 5G standard, we want to achieve order-of-magnitude performance enhancement on wireless digital signal processing kernels.

## Slide 2
Inductive Kernels
F( )=
F( )=
F( )=
Inductive Kernels
  QR, SVD, Cholesky, Solver
Challenges
  Poor vectorization
  Too small to be multi-threaded
12..32
Notes: Trip count and memory access pattern are determined by the inductive variable.

## Slide 3
Chart: General Purpose Processor Performance
| svd-12 | svd-24 | svd-32 | qr-12 | qr-24 | qr-32 | cho-12 | cho-24 | cho-32 | sol-12 | sol-24 | sol-32 | avg
dsp | 0.03 | 0.03 | 0.02 | 0.07 | 0.03 | 0.02 | 0.06 | 0.04 | 0.03 | 0.14 | 0.12 | 0.11 | 0.05
cpu | 0.1 | 0.08 | 0.08 | 0.07 | 0.06 | 0.03 | 0.07 | 0.06 | 0.04 | 0.21 | 0.06 | 0.06 | 0.07
gpu | 0.01 | 0.04 | 0.05 | 0.02 | 0.03 | 0.03 | 0.01 | 0.01 | 0.02 | 0.01 | 0.01 | 0.01 | 0.02
% of the ideal performance
25%
Notes: Mention what the y-axis is. Explicit!

## Slide 4: Our Goal: An Efficient, Flexible, and Specialized Architecture
Base Design: Spatial Architecture
Specialize Inductive Idioms
  Hybridizing PEs, Inductive Control, and Implicit Vector Padding
  Scale up with multiple lanes
REVEL: Reconfigurable Vector Lanes
  3.4x, and 17x speedup over existing spatial architectures, and general purpose processors
  2x power and half area comparing with ASIC collection
Sync
Sync
Private
Spad
Ctrl
XFER
Ctrl
Ctrl
Sync
Sync
Private
Spad
Ctrl
Shared Spad
Ctrl
XFER
Ctrl
Sync
Sync
Private
Spad
Ctrl
Notes: What we discover here is spatial architecture works well in this domain, but still can be enhanced.

## Slide 5: Outline
Background
  “Dataflow” or “Systolic”? A tradeoff between cost and flexibility
  Challenge 1: Synchronous Coordination
  Challenge 2: Overwhelmed Processing Elements
  Challenge 3: Overwhelmed Coordination
    Inductive Access
    Padding the Vectorization
REVEL: Reconfigurable Vector Lanes
Evaluation
Notes: There are 3 parts
In the 1st of my talk. 2 Prior architectures.
Explain their challenges.
New mechanism, and specialization.
Full stack evaluation.

## Slide 6: Spatial Architecture
✖️
✖️
➖
＋
>>
✖️
✖️
➖
＋
>>
Each PE is dedicated to one instruction
The timing of data arrival are determined when compilation
＋
>>
✖️
✖️
➖
Multiple instructions shared PE
Dynamically scheduled execution
Dependence Graph
Tagged Dataflow
Systolic
5.8x Area
4.2x Power
Architectures expose computing resource and on-chip network to programming interfaces
Notes: There are so many spatial architectures. We show two extremes here.
These two architectures are fundamentally different in two ways.

## Slide 7
Chart: Spatial Architecture Performance
| svd-12 | svd-24 | svd-32 | qr-12 | qr-24 | qr-32 | cho-12 | cho-24 | cho-32 | sol-12 | sol-24 | sol-32 | avg
systolic | 0.13 | 0.15 | 0.11 | 0.13 | 0.1 | 0.09 | 0.16 | 0.11 | 0.11 | 0.11 | 0.11 | 0.11 | 0.12
tagged dataflow | 0.27 | 0.26 | 0.19 | 0.5 | 0.22 | 0.17 | 0.69 | 0.65 | 0.6 | 0.56 | 0.35 | 0.28 | 0.35
% of the ideal performance
Notes: Dataflow works really well, but its high power/area penalty.

## Slide 8: Base Design: Systolic Architecture with Decoupled Data Access
Sync
Sync
Scratch Memory
Ctrl
XFER
Ctrl
Ctrl
✖️
✖️
➖
＋
>>
Arithmetic operations are offloaded onto spatial architecture
Data access are decoupled and coordinated by the controller
Synchronization buffers serve as interfaces between dynamic/static timing
Notes: Take our base systolic architecture, and analyze the challenges.

## Slide 9: Challenge 1: Non-uniform Produce/Consume Rate
for (j=0; j<n; ++j) {
x[j] = x[j]/a[j,j];
for (i=j+1; i<n; ++i)
x[i] -= x[j]*a[j,i];
}
Sync
Sync
Scratch Memory
Ctrl
XFER
Ctrl
Ctrl
✖️
➖
➗
1|(n-j-1)
produce|consume
Notes: Fundamentally systolic cannot do different rate.
Make it goes faster.

## Slide 10: Challenge 2: Overwhelmed Processing Elements
for (k=0; k<n; ++k) {
inv = 1.0/a[k,k];
invsqrt = 1.0/sqrt(a[k,k]);
for (j=k; j<n; ++j)
l[j,k] = a[k,j]*invsqrt;
for (j=k+1; j<n; ++j)
for (i=j; i<n; ++i)
a[j,i] -= a[k,i]*a[k,j]*inv;
}
10
Sync
Sync
Scratch Memory
Ctrl
XFER
Ctrl
Ctrl
✖️
✖️
✖️
-
√
➗
➗
Notes: If too big, timeplex, reconfig

## Slide 11: Challenge 3.1: Overwhelmed Coordination
Sync
Sync
Scratch Memory
Ctrl
XFER
Ctrl
Ctrl
✖️
➖
➗
for (j=0; j<n; ++j) {
x[j] = x[j]/a[j,j];
for (i=j+1; i<n; i+=2) {
x[i] -= x[j]*a[j,i];
}}
a[n:m,p:q]
Rectangular Slicing:
Triangular Slicing:
a[n-2:n]
a[j+3:n]
a[j+2:n]
a[j+1:n]
…
Notes: No built in way

## Slide 12: Challenge 3.2: Imperfect Loop Tiling
Sync
Sync
Scratch Memory
Ctrl
XFER
Ctrl
Ctrl
✖️
➖
➗
for (j=0; j<n; ++j) {
x[j] = x[j]/a[j,j];
for (i=j+1; i<n; i+=2) {
x[i] -= x[j]*a[j,i];
if (i+1<n) x[i+1] -= x[j]*a[j,i+1];
}}
✖️
➖
a[n:m,p:q]
Rectangular Slicing:
Triangular Slicing:
a[n-2:n]
a[j+3:n]
a[j+2:n]
a[j+1:n]
…

## Slide 13: Outline
Spatial Architecture
REVEL: Reconfigurable Vector Lane
  Specialization 1: Hybridizing processing elements
  Specialization 2: Coordinating non-uniform dependences
  Specialization 3: Inductive Access Intrinsics
  Specialization 4: Implicit vectorization predication
  Scalability: Larger Spatial or Multiple Lanes?
Evaluation
Notes: Emph the inductive here.

## Slide 14: Specialization 1: Hybridizing Systolic and Dataflow
for (k=0; k<n; ++k) {
inv = 1.0/a[k,k];
invsqrt = 1.0/sqrt(a[k,k]);
for (j=k; j<n; ++j)
l[j,k] = a[k,j]*invsqrt;
for (j=k+1; j<n; ++j)
for (i=j; i<n; ++i)
a[j,i] -= a[k,i]*a[k,j]*inv;
}
14
Sync
Sync
Scratch Memory
Ctrl
XFER
Ctrl
Ctrl
✖️
✖️
✖️
-
√
➗
➗
O(1)
O(n)
O(n²)
Notes: We give the spatial architecture the capability of having multiple concurrent regions.
It is OK, for Cholesky to offload all these regions since we only have seven instructions to offload.
When it comes to QR or SVD, they have much more instructions. We do not have enough dedicated PEs to fit them all. Also, it may cause PE under utilization if those operations with relatively low execution rate occupy a dedicated.

## Slide 15: Specialization 2: Coordinating Non-uniform Dependences
Sync
Sync
Scratch Memory
Ctrl
XFER
Ctrl
Ctrl
✖️
➖
➗
for (j=0; j<n; ++j) {
x[j] = x[j]/a[j,j];
for (i=j+1; i<n; ++i)
x[i] -= x[j]*a[j,i];
}
1|(n-j-1)
1|(n-j-1)

## Slide 16: Specialization 3: Inductive Memory Access
Sync
Sync
Scratch Memory
Ctrl
XFER
Ctrl
Ctrl
✖️
➖
➗
for (j=0; j<n; ++j) {
x[j] = x[j]/a[j,j];
for (i=j+1; i<n; i+=2) {
x[i] -= x[j]*a[j,i];
if (i+1<n) x[i+1] -= x[j]*a[j,i+1];
}}
a[n:m,p:q]
Rectangular Slicing:
Triangular Slicing:
a[n-2:n]
a[j+3:n]
a[j+2:n]
a[j+1:n]
…
a[k,j:n]

## Slide 17: Specialization 4: Implicit Vectorization Predication
Sync
Sync
Scratch Memory
Ctrl
XFER
Ctrl
Ctrl
✖️
➖
➗
for (j=0; j<n; ++j) {
x[j] = x[j]/a[j,j];
for (i=j+1; i<n; i+=2) {
x[i] -= x[j]*a[j,i];
if (i+1<n) x[i+1] -= x[j]*a[j,i+1];
}}
✖️
➖
Generate masks according to the
striding pattern
Triangular Slicing:
a[n-2:n]
a[j+3:n]
a[j+2:n]
a[j+1:n]
…
Notes: Take advantage of the awareness of the inner loop trip count implicitly predicate off that lane

## Slide 18: Scalability: A larger mesh or multiple lanes?
Sync
Sync
Scratch Memory
Ctrl
XFER
Ctrl
Ctrl
Sync
Sync
Private
Spad
Ctrl
XFER
Ctrl
Ctrl
Sync
Sync
Private
Spad
Ctrl
XFER
Ctrl
Sync
Sync
Private
Spad
Ctrl

## Slide 19: REVEL: Reconfigurable Vector Lanes
A centralized control core commands multiple lanes
  Predication based broadcast
  SIMT-like control commands
Each lane is independent to execute
Sync
Sync
Private
Spad
Ctrl
XFER
Ctrl
Ctrl
Sync
Sync
Private
Spad
Ctrl
Shared Spad
Ctrl
XFER
Ctrl
Sync
Sync
Private
Spad
Ctrl
Lane 0
Lane 1
01010101
a[k,j:n]
0
a[0,j:n]
1
a[1,j:n]
0
a[2,j:n]
Notes: Then here comes to the problem: how to add the Fus? How these added Fus are managed?
We want larger spatial accelerator or multiple duplicated instances, I mean lanes?
To sustain a larger spatial accelerator, we need higher bandwidth from the memory and more bookkeeping slots in the stream engine.
Moreover, compiling a larger spatial accelerator has exponentially larger solution space to explore. Thus, it seems lane is the right solution.

## Slide 20: Outline
Spatial Architecture
REVEL: Reconfigurable Vector Lanes
Evaluation
  Methodology
  Speedup

## Slide 21: Evaluation Methodology
Performance
  Gem5 RISCV in-order core integrated with a cycle-accurate spatial architecture simulator
    Extending the stream-dataflow ISA
  Baselines:
    Intel(R) Xeon(R) Silver 4116 @2.10GHz (Intel MKL)
    TI6678 DSP @1.25GHz (TI DSPLIB)
    NVIDIA Titan (cuBlas)
Power/Area
  Spatial Architecture implemented in Chisel
  Synthesized in Synopsys DC 28nm @1.25GHz
  SRAM power/area are estimated by CACTI.
Same peak performance
Chart: 
| CGRA Net | Trig Net | FUs | SPAD | VP/SE | Control Core
 | 0.48 | 0.16 | 0.56 | 0.48 | 0.24 | 0.04

## Slide 22
Chart: Speedup (Batch-8)
| svd-32 | qr-32 | cho-32 | sol-32 | fir-199x1024 | mm-48x16-64 | fft-1024 | gm
cpu | 3.55 | 1.19 | 1.29 | 0.51 | 1.11 | 0.59 | 0.4 | 0.96
gpu | 18.87 | 8.53 | 4.01 | 0.78 | 3.22 | 5.63 | 0.43 | 3.26
systolic | 5.05 | 4.18 | 3.38 | 0.97 | 4.95 | 3.6 | 1.19 | 2.83
tagged | 8.52 | 2.22 | 5.5 | 2.53 | 0.36 | 0.29 | 0.38 | 1.4
revel | 22.35 | 12.08 | 14.65 | 6.81 | 4.95 | 3.59 | 4.64 | 8.06

Speedup over the TI DSP (log scale)
Notes: Small first, and large second.
The result is log scaled by 10.
Make the y-axis.

## Slide 23
Chart: Speedup (Batch-1)
| svd-32 | qr-32 | cho-32 | sol-32 | fir-199x1024 | mm-48x16-64 | fft-1024 | gm
cpu | 3.55 | 1.19 | 1.29 | 0.51 | 1.11 | 0.59 | 0.4 | 0.96
gpu | 2.29 | 1.46 | 0.51 | 0.1 | 3.22 | 1.52 | 0.43 | 0.86
systolic | 5.05 | 4.18 | 3.38 | 0.97 | 29.78 | 26.91 | 1.19 | 4.88
dataflow | 8.52 | 7.97 | 18.73 | 2.53 | 2.3 | 2.35 | 0.38 | 3.51
revel | 22.35 | 22.53 | 30.36 | 6.81 | 29.78 | 26.91 | 4.64 | 16.86
Speedup Over the TI DSP (log scale)

## Slide 24: Conclusion
According to our results, REVEL and its hybrid architecture is a promising next-generation digital signal processing architecture.
More broadly, our work demonstrates the importance of considering multiple execution models.

## Slide 25
Chart: Impact of each Specialization
| cho.-12 | cho.-16 | cho.-24 | cho.-32 | qr-12 | qr-16 | qr-24 | qr-32 | sol.-12 | sol.-16 | sol.-24 | sol.-32 | svd-12 | svd-16 | svd-24 | svd-32 | fft-64 | fft-128 | fft-512 | fft-1024
Base | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Induc. Coord. | 0.10664 | 0.12771 | 0.21451 | 0.14562 | 0.029792 | 0.10165 | 0 | 0.064717 | 0 | 0 | 0 | 0 | 0.0019303 | 0.031995 | 0.013184 | 0.011676 | 2.6085 | 2.5769 | 2.8801 | 2.8927
Hybrid Df/Sys. | 2.169 | 1.9431 | 0.8814 | 0.6875 | 0.91697 | 0.8252 | 0.55735 | 0.50441 | 5.6308 | 5.7727 | 5.897 | 6.0116 | 2.6964 | 3.1275 | 3.0412 | 3.273 | 0 | 0 | 0 | 0
Vec. Pred. | 2.7323 | 3.1125 | 3.462 | 2.5028 | 1.6093 | 1.5594 | 1.4575 | 1.2488 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Notes: Here is the effect of implicit masking. QR and Cholesky are helped the most because of their shrinking matrix.
Solver can already be efficiently executed by manually managing the padding.
SVD is too compute intensive to vectorize.

## Slide 26: Compilation: A Semi-Automated Approach

## Slide 28: Scalability: A larger mesh or multiple lanes?
Sync
Sync
Exponentially longer time to compile the spatial architecture
Longer reconfiguration for the whole spatial architecture
Longer routing path increases the latency of communication
Scratch Memory
Ctrl
XFER
Ctrl
Ctrl